## Slide 1
Jin Uk Ko, Yann De Coster
Arch Bridge Optimization Under Uniform Pressure Considering Fracture Strength
Probabilistic Engineering Analysis and Design Term Project, 2017.12.11, Seoul, Korea

## Slide 2
Design Optimization
Motivation
Sensitivity Analysis
Problem Statement & Model
Reliability-Based Design Optimization
01
02
03
04
05

## Slide 3
Motivation

## Slide 4
Motivation
Bridge Name | Nation | Year | Type | Length | Nb of Arches | Cause
Wilson | France | 1978 | Dimension stone | 434 [m] | 15 | Tremendous flood which exceeded the design flood; plus scouring due to running water
Wharfe | UK | 2015 | Magnesian Limestone | 26 [m] | 5 | 
Capilano River | Canada | 1917 | Wood/Concrete | 77 [m] | 4 | 
Xiushui County | China | 2016 | Stones | 185 [m] | 8 | 
Wilson Bridge, Tours (1978, France)
← Cost:
35 M francs
(~ €18,4 M)
3 deaths ,
2 injuries →
Risk of Failure in Bridge
Xiushui County Bridge (2016, China)

## Slide 5
Problem Statement
& Model

## Slide 6
Problem Statement & Model
Problem Statement and Model
L
Subject to
Where
is design variable vector

## Slide 7
Problem Statement & Model
Random Variables
Random Variable | Mean | Standard Deviation | Distribution Type | Lower Design Bound | Upper Design Bound
x1 [m] | 2 | 0.5 | normal | 4 | 10
x2 [m] | 8.5 | 1.5 | normal | 10 | 20
x3 [m] | 2.25 | 0.5 | normal | 1 | 4
x4 [m] | 17 | 2.5 | normal | 24 | 36
E [GPa] | 20 | 2.0 | normal | 10 | 30
[kg/m3] | 2000 | 20 | normal | 1800 | 2200
P [kPa] | 500 | 10 | normal | 400 | 600
Poisson ratio | Deterministic: 0.15 |  |  |  | 
Length [m] | Deterministic: 100 |  |  |  | 
Thickness [m] | Deterministic: 12 |  |  |  | 
Random Variable | Mean | Standard Deviation | Distribution Type | Lower Design Bound | Upper Design Bound
x1 [m] | 2 | 0.5 | normal | 4 | 10
x2 [m] | 8.5 | 1.5 | normal | 10 | 20
x3 [m] | 2.25 | 0.5 | normal | 1 | 4
x4 [m] | 17 | 2.5 | normal | 24 | 36
E [GPa] | 20 | 2.0 | normal | 10 | 30
 | 2000 | 20 | normal | 1800 | 2200
P [kPa] | 500 | 10 | normal | 400 | 600
Poisson ratio | Deterministic: 0.15 |  |  |  | 
Length [m] | Deterministic: 100 |  |  |  | 
Thickness [m] | Deterministic: 12 |  |  |  | 
L

## Slide 8
Problem Statement & Model
Reviewing the Project
Mesh Information:
  Mesh Size: about 1 [m]
  DoF: 8076
Analysis Time: 3 [sec]
The fixed constraints: both sides & three bottom edges.
COMSOL Convergence Test
finer
coarser

## Slide 9
Design Optimization

## Slide 10
Design Optimization
Design Variables | Initial | Optimum
x1 [m] | 7 | 7
x2 [m] | 15 | 13.3403
x3 [m] | 2.5 | 2.0021
X4 [m] | 30 | 24
Area [m2] | 2143.14 | 1734.08
Tolerance: 1e-9
Iteration: 8 & F-count: 104
Time: 269.793[sec]
Area deceases 19%
Design Optimization Result

## Slide 11
Design Optimization
Reliability of Initial Design Result
PDF & CDF of Maximum Von Mises Stress
Reliability with several methods
Methods | MCS | FORM | SORM | RIA
Maximum Von Mises Stress | 0.2093 | 0.2229 | 0.2229 | 0.2275

## Slide 12
Design Optimization
Reliability of Design Optimization Result
PDF & CDF of Maximum Von Mises Stress
Reliability with several methods
Methods | MCS | FORM | SORM | RIA
Maximum Von Mises Stress | 0.4610 | 0.5000 | 0.5001 | 0.5000

## Slide 13
Reliability Based
Design Optimization

## Slide 14
Reliability Based Design Optimization
Design Variables | Initial | RBDO (PMA) | RBDO (RIA)
x1 [m] | 7 | 10 | 10
x2 [m] | 15 | 11.2586 | 11.2342
x3 [m] | 2.5 | 1.6302 | 1.5164
X4 [m] | 30 | 24.1577 | 24.2236
Area [m2] | 2143.14 | 1944.14 | 1957.73
Reliability Based Design Optimization Result (From Initial Design)

## Slide 15
Reliability Based Design Optimization
Reliability of Reliability Based Design Optimization Result-PMA
PDF & CDF of Maximum Von Mises Stress (Starting from Initial Design)
Reliability with several algorithms
Constraint | MCS | FORM | SORM | RIA
Maximum Von Mises Stress | 0.9952 | 0.9901 | 0.9905 | 0.9924

## Slide 16
Reliability Based Design Optimization
Reliability of Reliability Based Design Optimization Result-RIA
PDF & CDF of Maximum Von Mises Stress (Starting from Initial Design)
Reliability with several algorithms
Constraint | MCS | FORM | SORM | RIA
Maximum Von Mises Stress | 0.9963 | 0.9919 | 0.9920 | 0.9922

## Slide 17
Reliability Based Design Optimization
Design Variables | DDO | RBDO (PMA) | RBDO (RIA)
x1 [m] | 7 | 10 | 10
x2 [m] | 13.3403 | 11.2201 | 11.2152
x3 [m] | 2.0021 | 1.5302 | 1.5264
X4 [m] | 24 | 24.1868 | 24.2108
Area [m2] | 1734.07 | 1954.51 | 1957.45
Reliability Based Design Optimization Result (From DDO)
Notes: Tolerance: 1e-9
Iteration: 7
F-count: 111
Time (PMA): 18.3 [hr]

## Slide 18
Reliability Based Design Optimization
Reliability of Reliability Based Design Optimization Result-PMA
PDF & CDF of Maximum Von Mises Stress (Starting from DDO)
Reliability with several algorithms
Constraint | MCS | FORM | SORM | RIA
Maximum Von Mises Stress | 0.9926 | 0.9913 | 0.9914 | 0.9958

## Slide 19
Reliability Based Design Optimization
Reliability of Reliability Based Design Optimization Result-RIA
PDF & CDF of Maximum Von Mises Stress (Starting from DDO)
Reliability with several algorithms
Constraint | MCS | FORM | SORM | RIA
Maximum Von Mises Stress | 0.9964 | 0.9939 | 0.9942 | 0.9935

## Slide 20
Sensitivity Analysis

## Slide 21
Sensitivity Analysis
Sensitivity Analysis for RBDO results
Maximum Von Mises Stress
Random variables | x1 [m] | x2 [m] | x3 [m] | x4 [m]
PMA (Initial) | 0.1682 | -0.7126 | -0.1716 | 0.0006
RIA (Initial) | 0.1458 | -0.3731 | -0.1075 | 1.0804
PMA (DDO) | -0.4560 | -1.0141 | -0.3467 | 0.1998
RIA (DDO) | 0.1564 | -0/6714 | -0.6543 | 0.4384
L
As x4 increases, Reliability increases
As x2, x3 increase, Reliability decreases
negative
negative
positive
positive
(except 3th)